1999 U Value Question

| U Value Table |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Element/Material | Conductivity (K) | Resistivity (1/K) | Thickness (m) | Resistance ( R ) |  |
| Ext. Surface R |  |  |  | 0.053 |  |
| Int. Surface R |  |  |  | 0.123 |  |
| Cavity R |  |  |  | 0.176 |  |
| Facing Brick | 1.4 | 0.714 | 0.1 | 0.0714 |  |
| Aerated Conc Block | 0.22 | 4.545 | 0.1 | 0.4545 |  |
| LW Plaster | 0.16 | 6.25 | 0.015 | 0.09375 |  |
| Urethane Boards | 0.033 | 30.3030303 | 0.035 | 1.060606061 |  |
|  |  |  | Total R | 2.032256061 |  |
|  |  | U Value | 1/Total R = | 0.492063977 | w/m²K |

Part B on next page

R of Wall =  2.0322

R of Cavity = 0.176

R of partial fill insulation =  1.060,    add the 2 Rs

Wall minus cavity R  and Insulation = 2.0322 – 1.236  = 0.796

| Element/Material | Conductivity (K) | Resistivity (1/K) | Thickness (m) | Resistance ( R ) |  |
| --- | --- | --- | --- | --- | --- |
| Insulation (Blown fibre) |  | 35.714 | 0.1 | 3.5714 |  |

Add the R of the wall minus partial fill insulation and cavity R an add  the R of the filled cavity.

  - +  3.5714  =  4.3674

1  / 4.3674 = U value = 0.2289 W/m² K