U Value 2000

| U Value Table |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Element/Material | Conductivity (K) | Resistivity (1/K) | Thickness (m) | Resistance ( R ) |  |
| Ext. Surface R |  |  |  | 0.0800 |  |
| Int. Surface R |  |  |  | 0.1200 |  |
| Air Space |  |  |  | 0.1500 |  |
| 5mm Glass | 1.02 | 0.980 | 0.005 | 0.0049 |  |
| 5mm Glass | 1.02 | 0.980 | 0.005 | 0.0049 |  |
|  |  |  | Total R | 0.3598 |  |
|  |  | U Value | 1/Total R = | 2.779 | W/m² ºC |

Heat Loss Formula,

U Value  X  Area  X  Temp. Diff.  =    Ans. Watts or Joules per second

2.779  X  6  X  20  =  333.48 Watts