U Value 2003

| U Value Table |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Element/Material | Conductivity (K) | Resistivity (1/K) | Thickness (m) | Resistance ( R ) |  |
| Ext. Surface R |  |  |  | 0.048 |  |
| Int. Surface R |  |  |  | 0.122 |  |
| Air Space |  |  |  | 0.17 |  |
| Block Int | 1.44 | 0.694444444 | 0.1 | 0.069444444 |  |
| Brick Ext | 1.32 | 0.757575758 | 0.1 | 0.075757576 |  |
| Plaster Int | 0.43 | 2.325581395 | 0.016 | 0.037209302 |  |
|  |  |  | Total R | 0.522411323 |  |
|  |  | U Value | 1/Total R = | 1.914200472 | W/m² ºC |

Option 1,  Fill the cavity

| Element/Material | Conductivity (K) | Resistivity (1/K) | Thickness (m) | Resistance ( R ) |
| --- | --- | --- | --- | --- |
| Urea Formaldahyde foam | 0.04 | 25 | 0.075 | 1.875 |

Total R  =  Old R   +   R of Foam   minus  R of Cavity

=  0.5224   +   1.875   minus   0.170

=  2.22739

U Value   =   1/Total R   =   0.4489 W/m² ºC

Option 2, Dry Line using insulated plasterboard sheeting

| Element/Material | Conductivity (K) | Resistivity (1/K) | Thickness (m) | Resistance ( R ) |
| --- | --- | --- | --- | --- |
| Rigid Urethane | 0.023 | 43.47826087 | 0.05 | 2.173913043 |
| Plasterboard | 0.16 | 6.25 | 0.0125 | 0.078125 |
|  |  |  | Total R | 2.252038043 |

Total R  =  Old R   +   R of Urethane and plasterboard

=   0.5224  +    2.2520   =    2.7744

U Value   =   1/Total R   =   1 / 2.7744   =   0.3604 W/m² ºC

Combination of Option 1  +  Option 2

Total R   =   R from Option 1   +   R of Insulated slab

=   2.22739   +   2.252

=   4.47939

U Value   =   1/Total R   =   1 /  4.47939   =   0.2232 W/m² ºC