U Value 2007

Part A

| U Value Table |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Element/Material | Conductivity (K) | Resistivity (1/K) | Thickness (m) | Resistance ( R ) |  |
| Ext. Surface R |  |  |  | 0.048 |  |
| Cavity R |  |  |  | 0.170 |  |
| Int. Surface R |  |  |  | 0.122 |  |
| Ext. Plaster | 0.43 | 2.32558 | 0.016 | 0.037 |  |
| Block outer leaf | 1.44 | 0.6944 | 0.1 | 0.069 |  |
| Block inner leaf | 1.44 | 0.6944 | 0.1 | 0.069 |  |
| Int. Plaster | 0.43 | 2.32558 | 0.013 | 0.030 |  |
|  |  |  | Total R | 0.545 |  |
|  |  | U Value | 1/Total R = | 1.8348 | W/m² ºC |

Part B

Calculate the rate of heat loss

Area (m.sq) x  Temp. diff  x  u value  =   w/sec  or  Joules / sec

145  X  13 X  1.8248  =  3,439.75 w/sec  or  Joules / sec

Use the Heating period    and    multiply by rate of heat loss

Heating period per annum

10  X  7  X  42 = 2,940

6o  x  6o  x  2,940   =  10,584,000  X  3,439.75  divided by 1000 to get Kw/KJ

=  36,406,314  Kj

1 litre of Oil   =  37,350 KJ

Therefore

36,406,314  divided by 37,350  =  no. of litre  =  974.73 Litres

@ 0.68 cent / Litre =  € 662.82c  = annual heating cost

Part C